## Slide 1: BATTLEBOT Team 3
Capstone 1 Preliminary Design Review

## Slide 2: Who are We?
Group members
  Ivan Albert
  Nishagar Raventhiran
  Cole Trugman
Advisor
  James Black
Course
  Capstone 1, EMEC 489

## Slide 3: The Competition
Design robot to battle two other opposing robots
Attempt to disable opponents
Ready for any weather
Avoid obstacles in the arena
www.broadcastingcable.com

## Slide 4: Level 1 Requirements
Less than 25 lbs
Fit in 18 in cube
Adheres to weapon limitations
Costs less than $1000
Able to run for 3 minutes on one charge
Not a pre assembled robot or toy
Must include a master power disconnect switch

## Slide 5: Background
Lessons from televised battlebot competitions
Electrical Controls
Structural Materials
Mobility

## Slide 6: Design Specifications
Design specifications were categorized as follows:
Offensive/defensive Specifications
Functional Specifications
Physical Specifications

## Slide 7: Offensive/defensive Specifications
Minimum force given by the robot is 20 lb.
Robot must withstand a minimum pushing force of 20 lb as well as 25 lb gravitational force .
Minimum speed of the robot should be 1 ft/s.

## Slide 8: Functional Specifications
Have to have enough battery power to run through whole competition
The turning radius of the robot has to be at most 3 ft
Control system must interface with driving motors, and the remote control
Range must be reliable up to 33.5 ft

## Slide 9: Physical Specifications
Maximum allowable weight is 25 lb
Must be able to stow into an 18” cube
Radius edges must be greater than ⅛”
Keep the cost between $500 and $1000

## Slide 10: Design Evaluation: Drive System
Drive System | Total Points
Dead Axle: | X
Wheels | 6
Tank Treads | 2
Live Axle | 2
Omni Wheels | 0
www.servomagazine.com

## Slide 11: Design Evaluation: Electrical Control System
Electronic Control System | Total Points
Microcontroller: | X
Bluetooth | 5
Radio | 4
Wi-Fi | 3
Off the Shelf RC Parts | 3
www.raspberrypi.org
www.adafruit.com

## Slide 12: Design Evaluation: Weapon System
Weapon System | Total Points
Roller | 5
Hammer | 4
“Hermit Crab” | 2
Hydraulic Wedge | 0
Spatula | 0
www.youtube.com/channel/UC_IpSl6O_-IRAA6fiNs05Gg
www.design1st.com

## Slide 13: Design Evaluation: Armor
Armor | Total Points
Aluminum | 3
1018 Steel | 2
UHMWPE | 1
AR400 Steel | 0
www.thestreet.com
www.ar500armor.com

## Slide 14: Design Alternatives
Design | Drive System | Electrical System | Weapon | Armor | Total Points
Design 1 | Dead Axle: Wheels | Micro: Bluetooth | Roller | Aluminum | 19
 | 6 | 5 | 5 | 3 | 
Design 2 | Omni Wheels | Micro: Radio | Hammer | UHMWPE | 9
 | 0 | 4 | 4 | 1 | 
Design 3 | Dead Axle: Wheels | Micro: Bluetooth | Hydraulic Wedge | 1018 Steel | 13
 | 6 | 5 | 0 | 2 | 

## Slide 15: Chosen Design
Roller as main weapon system
Wedge in rear
Dead axle drive
Aluminum with layer of Ar400 (where applicable)
Reprogrammable microcontroller

## Slide 16: Timeline
November 26: Have CDR presentation ready
November 30: Finish drawings/models/Manufacturing plan
December 3: Complete written report
December 10: Buy materials and components
December 14: Start manufacturing
January: Start programming microcontroller.
March: Integrate subsystems
April: Testing robot
May: Competition day